## Slide 1: BIER Bit Indexed Explicit Replication Hackathon
IJsbrand Wijnands
Greg Shepherd

## Slide 3: The BIER Epiphany
Only encode the end-receivers in the packet header.
  Not the intermediate nodes.
Assign end-receivers a Bit Position from a Bit String.
  The smallest identifier possible.
Encode the Bit String in the packet header.
  Using some sort of encapsulation.
Create a Bit Forwarding Table on all BIER nodes to allow multicast packet forwarding using the Bit String in the packet.
  Derived from the RIB, SPF based.
Bit Indexed Explicit Replication (BIER).

## Slide 4: IETF
The BIER idea was presented in a BOF at the IETF in Hawaii.
  November 2014.
A BIER Working Group has been formed (bier@ietf.org)
Vendors collaborating;
  Cisco
  Ericsson
  Alcatel-Lucent
  Juniper
  Huawei

## Slide 5: IETF drafts
draft-shepherd-bier-problem-statement-00
draft-ietf-bier-architecture-01
draft-ietf-bier-use-cases-00
draft-ietf-bier-mpls-encapsulation-01
draft-ietf-bier-mvpn-01
draft-ietf-ospf-bier-extensions-00
draft-ietf-bier-isis-extensions-00
draft-eckert-bier-te-arch-00
draft-xu-idr-bier-extensions-00

## Slide 6: Solution Overview

## Slide 7: Basic Idea BIER
BitString
BIER Domain
LSA
1 - A/32
LSA
5 – E/32
LSA
4 – D/32
LSA
3 – C/32
LSA
2 – B/32
1. Assign a unique Bit Position from a BitString to each BFER in the BIER domain.
2. Each BFER floods their Bit Position to BFR-prefix mapping using the IGP (OSPF, ISIS)
1
2
3
4
5
B/32
A/32
C/32
D/32
E/32
1
2
3
4
5

## Slide 8: Basic Idea BIER
BIER Domain
1. Assign a unique Bit Position from a mask to each edge router in the BIER domain.
2. Each edge router floods their bit-position-to-ID mapping with a new LSA – OSPF or ISIS
3. All BFR’s use unicast RIB to calculate a best path for each BFR-prefix
BitMask | Nbr
0011 | A
0100 | B
1000 | C
4. Bit Positions are OR’d together to form a Bit Mask per BFR-nbr
5. Packets are forwarded and replicated hop-by-hop using the Bit Forwarding Table..

## Slide 9: Bit Index Forwarding Table
D, F and E advertise their Bit positions in the IGP (flooded).
A, B and C know the mapping between the Bit and RID,
Based on shortest path route to RID, the Bit Mask Forwarding Table is created.
C
A
B
D
F
E
BM | Nbr
0111 | B
BM | Nbr
0011 | C
0100 | E
BM | Nbr
0001 | D
0010 | F
0001
0010
0100
BM | Nbr
0011 | C
 | B
BM-ER
BM-ER
BM-ER

## Slide 10: Forwarding Packets
C
A
B
D
F
E
Overlay session
0001
BM | Nbr
0111 | B
BM | Nbr
0011 | C
0100 | E
BM | Nbr
0001 | D
0010 | F
0001
0001
0001
AND
AND
AND
0001
0001
0010
0100
&0011
&0111
&0001
 | Nbr
0011 | C
 | B

## Slide 11: Forwarding Packets
C
A
B
D
F
E
Overlay session
 | Nbr
0111 | B
 | Nbr
0011 | C
0100 | E
 | Nbr
0001 | D
0010 | F
0001
0101
0001
AND
AND
0100
0100
AND
0101
0001
0001
0010
0100
&0011
&0111
&0001
&0100
 | Nbr
0011 | C
 | B
AND

## Slide 12: Forwarding Packets
C
A
B
D
F
E
 | Nbr
0111 | B
 | Nbr
0011 | C
0100 | E
 | Nbr
0001 | D
0010 | F
0011
0111
0001
AND
AND
0100
0010
0010
AND
0111
0001
0100
0001
0010
0100
 | Nbr
0011 | C
 | B
&0011
&0111
&0001
&0100
&0010
AND
Overlay session

## Slide 13: How many Bits and Where?
The number of multicast egress routers that can be addressed is depending on the number of Bits that can be included in the BitString
The BitString length is depending on the encapsulation type and router platform.
Current focus is on MPLS.
BIER Label | BIER Header | VPN Label | Payload
MPLS Label
IPv4/IPv6/L2
Upstream Label
BIER header

## Slide 14: Hackathon idea’s Not limited to 

## Slide 15: BIER areas to explore
Methods to encode the BitString
  Dallas, IETF 92 BIER encoding in IPv6 for HomeNet
Provider
Enterprise
HomeNet!
  See above
IOT
  Resource discovery over BIER
SDN integration, ODL, etc..
  Central bit assignment, flow membership, policy, etc..
LISP control plane for BIER membership